## Slide 1
COURSE:
Processors and Controllers
COURSE CODE:24EC2106
Topic:
CO 2- 8051
Department of ECE

## Slide 2
Microcontroller
8051

## Slide 3: The necessary tools for a microprocessor/controller
CPU
General-Purpose Micro-processor
RAM
ROM
I/O Port
Timer
Serial
COM
Port
Data Bus
Address Bus
General-Purpose Microprocessor System
RAM
ROM
I/O Port
Timer
Serial COM Port
Microcontroller
CPU
Example：Motorola’s 6811, Intel’s 8051, Zilog’s Z8 and PIC 16X

## Slide 4: Block Diagram of 8051
CPU
On-chip RAM
On-chip ROM for program code
4 I/O Ports
Timer 0
Serial Port
OSC
Interrupt Control
External interrupts
Timer 1
Timer/Counter
Bus Control
TxD RxD
P0 P1 P2 P3
Address/Data
Counter Inputs

## Slide 5: Features of 8051 Microcontroller
An 8051 microcontroller comes bundled with the following features −
4KB bytes on-chip program memory (ROM)
128 bytes on-chip data memory (RAM)
Four register banks
128 user defined software flags
8-bit bidirectional data bus
16-bit unidirectional address bus
32 general purpose registers each of 8-bit
16 bit Timers (usually 2, but may have more or less)
Three internal and two external Interrupts
Four 8-bit ports,(short model have two 8-bit ports)
16-bit program counter and data pointer
8051 may also have a number of special features such as UARTs, ADC, Op-amp, etc.

## Slide 6: Architecture of 8051

## Slide 7
Comparison of the 8051 Family Members
Notes: versatility 多用途的: any number of applications for PC

## Slide 8
Pin Description of the 8051

## Slide 9
Port 3 Alternate Functions

## Slide 10: RESET Value of Some 8051 Registers:
0000
DPTR
07
SP
00
PSW
00
B
00
ACC
0000
PC
Reset Value
Register
RAM are all zero.

## Slide 11: Registers

## Slide 12
RAM memory space allocation in the 8051
7FH
30H
2FH
20H
1FH
17H
10H
0FH
07H
08H
18H
00H
Register Bank 0
(Stack) Register Bank 1
Register Bank 2
Register Bank 3
Bit-Addressable RAM
Scratch pad RAM

## Slide 19: 8051 Flag bits and the PSW register

## Slide 20
8051 Flag bits and the PSW register

## Slide 21: 8051 Flag bits and the PSW register

## Slide 22: 8051 PSW BANK SELECTION

## Slide 23: 8051 PSW BANK SELECTION

## Slide 24: Stack in the 8051
The register used to access the stack is called SP (stack pointer) register.
The stack pointer in the 8051 is only 8 bits wide, which means that it can take value 00 to FFH. When 8051 powered up, the SP register contains value 07.
7FH
30H
2FH
20H
1FH
17H
10H
0FH
07H
08H
18H
00H
Register Bank 0
(Stack) Register Bank 1
Register Bank 2
Register Bank 3
Bit-Addressable RAM
Scratch pad RAM

## Slide 25: Example of STACK operation: MOV R6,#25H MOV R1,#12H MOV R4,#0F3H PUSH 6 PUSH 1 PUSH 4
0BH
0AH
09H
08H
Start SP=07H
25
0BH
0AH
09H
08H
SP=08H
12
25
0BH
0AH
09H
08H
SP=09H
F3
12
25
0BH
0AH
09H
08H
SP=0AH

## Slide 26: 8051- Addressing Modes Immediate Register Direct Register Indirect Indexed

## Slide 27: Immediate Addressing Mode MOV A,#65H MOV A,#’A’ MOV R6,#65H MOV DPTR,#2343H MOV P1,#65H

## Slide 28: Register Addressing Mode MOV Rn, A ;n=0,..,7 ADD A, Rn MOV DPL, R6 MOV DPTR, A MOV Rm, Rn

## Slide 29: Direct Addressing Mode Although the entire of 128 bytes of RAM can be accessed using direct addressing mode, it is most often used to access RAM loc. 30 – 7FH. MOV R0, 40H MOV 56H, A MOV A, 4 ; ≡ MOV A, R4 MOV 6, 2 ; copy R2 to R6 ; MOV R6,R2 is invalid ! SFR register and their address MOV 0E0H, #66H ; ≡ MOV A,#66H MOV 0F0H, R2 ; ≡ MOV B, R2 MOV 80H,A ; ≡ MOV P1,A

## Slide 30: Register Indirect Addressing Mode In this mode, register is used as a pointer to the data. MOV A,@Ri ; move content of RAM loc. Where address is held by Ri into A ( i=0 or 1 ) MOV @R1,B In other word, the content of register R0 or R1 is sources or target in MOV, ADD and SUBB instructions. Example: Write a program to copy a block of 10 bytes from RAM location starting at 40H to RAM location starting at 60H. Solution: MOV R0,#40H ; source pointer MOV R1,#60H ; destination pointer MOV R2,#10 ; counter BACK: MOV A,@R0 MOV @R1,A INC R0 INC R1 DJNZ R2,BACK

## Slide 31: Indexed Addressing Mode And On-Chip ROM Access This mode is widely used in accessing data elements of look-up table entries located in the program (code) space ROM at the 8051 MOVC A,@A+DPTR A= content of address A +DPTR from ROM Note: Because the data elements are stored in the program (code ) space ROM of the 8051, it uses the instruction MOVC instead of MOV. The “C” means code.

## Slide 32: Example Programs

## Slide 33: Example Programs

## Slide 34: Example Programs

## Slide 35: Example Programs

## Slide 36: 8051- INSTRUCTION SET
Data transfer instructions.
Arithmetic instructions.
Logical instructions.
Logical instructions with bits.
Branch instructions.

## Slide 37: Data transfer instructions:
MOV Direct, Direct
MOV Direct,@Ri
MOV Direct,#Data
MOV @Ri,A
MOV @Ri,Direct
MOV @Ri,#Data
MOV DPTR,#Data16
MOVX A,@Ri
MOVX A,@DPTR
MOV A,Rn
MOV A, Direct
MOV A,@Ri
MOV A,#Data
MOV Rn,A
MOV Rn,Direct
MOV Rn,#Data
MOV Direct,A
MOV Direct, Rn

## Slide 38: Data transfer instructions:
PUSH Direct
POP Direct
XCH A,Rn
XCH A, Direct
XCH A,@Ri
XCHD A,@Ri
MOVX @Ri,A
MOV @DPTR,A

## Slide 39: Arithmetic instructions:
ADD A,Rn
ADD A,Direct
ADD A,@Ri
ADD A,#Data
ADDC A,Rn
SUBB A, Direct
SUBB A,@Ri
SUBB A,#Data
INC A
INC Rn
INC Direct
INC @Ri
DEC A
DEC Rn
SUBB A,Rn
ADDC A, Direct
ADDC A,@Ri
ADDC A,#Data

## Slide 40: Arithmetic instructions:
DEC Direct
DEC @Ri
INC DPTR
MUL AB
DIV AB
DA A

## Slide 41: Logical instructions:
ORL A,#Data
ORL Direct,A
ORL Direct,#Data
XRL A,Rn
XRL A,Direct
XRL A,@Ri
XRL A,#Data
XRL Direct,A
XRL Direct,#Data
ANL A,Rn
ANL A,Direct
ANL A,@Ri
ANL A,#Data
ANL Direct,A
ANL Direct,#Data
ORL A,Rn
ORL A,Direct
ORL A,@Ri

## Slide 42: Logical instructions:
CLR A
CPL A
RL A
RLC A
RR A
RRC A
SWAP A

## Slide 43: Boolean Variable Manipulation instructions:
CLR C
CLR bit
SETB C
SETB bit
CPL C
CPL bit
ANL C,bit
ANL C,/bit
ORL C,bit
ORL C,/bit
MOV C,bit
MOV bit,C
JC rel
JNC rel
JB bit,rel
JNB bit,rel
JBC bit,rel

## Slide 44: Program branching instructions:
ACALL addr11
LCALL addr16
RET
RETI
AJMP addr11
LJMP addr16
SJMP rel
JMP @A+DPTR
JZ rel
JNZ rel
CJNE A,direct,rel
CJNE A,#data,rel
CJNE Rn,#data,rel
CJNE @Ri,#data,rel
DJNZ Rn,rel
DJNZ direct,rel
NOP

## Slide 45: MUL & DIV MUL AB ;B|A = A*B MOV A,#25H MOV B,#65H MUL AB ;25H*65H=0E99 ;B=0EH, A=99H DIV AB ;A = A/B, B = A mod B MOV A,#25H MOV B,#10H DIV AB ;A=2, B=5

## Slide 46: Rotate EXAMPLE: RR: RRC: RL: RLC:
C
C

## Slide 47: 8051 INSTRUCTION SET
ACALL: Absolute Call
ADD, ADDC: Add Acc. (With Carry)
AJMP: Absolute Jump
ANL: Bitwise AND
CJNE: Compare & Jump if Not Equal
CLR: Clear Register
CPL: Complement Register
DA: Decimal Adjust
DEC: Decrement Register
DIV: Divide Accumulator by B
DJNZ: Dec. Reg. & Jump if Not Zero
INC: Increment Register
JB: Jump if Bit Set
JBC: Jump if Bit Set and Clear Bit
JC: Jump if Carry Set
JMP: Jump to Address
JNB: Jump if Bit Not Set
JNC: Jump if Carry Not Set
JNZ: Jump if Acc. Not Zero
JZ: Jump if Accumulator Zero
LCALL: Long Call
LJMP: Long Jump
MOV: Move Memory
MOVC: Move Code Memory
MOVX: Move Extended Memory
MUL: Multiply Accumulator by B
NOP: No Operation
ORL: Bitwise OR
POP: Pop Value From Stack
PUSH: Push Value Onto Stack
RET: Return From Subroutine
RETI: Return From Interrupt
RL: Rotate Accumulator Left
RLC: Rotate Acc. Left Through Carry
RR: Rotate Accumulator Right
RRC: Rotate Acc. Right Through Carry
SETB: Set Bit
SJMP: Short Jump
SUBB: Sub. From Acc. With Borrow
SWAP: Swap Accumulator Nibbles
XCH: Exchange Bytes
XCHD: Exchange Digits
XRL: Bitwise Exclusive OR
Undefined: Undefined Instruction

## Slide 48: TIMERS
The 8051 has two timers:
TIMER 0
TIMER 1
TIMER 0
TIMER 1

## Slide 50: TMOD Register
Gate : When set, timer only runs while INT(0,1) is high.
C/T : Counter/Timer select bit.
M1 : Mode bit 1.
M0 : Mode bit 0.

## Slide 51: TCON Register (BIT ADRESSABLE REG)
TCON.7 - TF1: Timer 1 overflow flag.
TCON.6 - TR1: Timer 1 run control bit.
TCON.5 - TF0: Timer 0 overflag.
TCON.4 - TR0: Timer 0 run control bit.
TCON.3 - IE1: External interrupt 1 edge flag.
TCON.2 - IT1: External interrupt 1 type flag.
TCON.1 - IE0: External interrupt 0 edge flag.
TCON.0 - IT0: External interrupt 0 type flag.

## Slide 52: Concept of timer

## Slide 53: Mode 1 Programming
Load the TMOD value register indicating which timer (Timer0 or Timer1) is to be used and which timer mode is selected.
Load registers TL & TH with initial count values.
Start the timer
Keep monitoring the timer flag(TF)
Stop the timer.
Clear TF for next round .
Go back to step 2 to load TH & TL again
NOTE: MODE 0 is exactly like mode-1 except that it is 13-bit timer instead 16-bit. The 13-bit timer/counter can hold values between 0000H to 1FFFH in TH-TL.

## Slide 54: Mode 2 Programming
Load the TMOD value register indicating which timer (Timer0 or Timer1)is to be used, and select the timer mode (mode-2).
Load the TH register with the initial count value.
Start the timer.
Keep monitoring TF timer flag
After it becomes “1” then clear the TF flag
Go back to step 4 , since mode 2 is auto - reload

## Slide 55: Example program for Mode1
ORG 0H
MOV TMOD,#00000001B
BACK: MOV TL0,#0F0H
MOV TH0,#0FFH
CPL P1.0
ACALL DELAY
SJMP BACK
DELAY:SETB TR0
HERE: JNB TF0, HERE
CLR TR0
CLR TF0
RET
END

## Slide 56: Example program for Mode2
ORG 0H
MOV TMOD,#00100000B
MOV TH1, #05H
SETB TR1
HERE: JNB TF1, HERE
CPL P2.0
CLR TF1
SJMP HERE
END