## Slide 1
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
SESSION - 3

## Slide 2
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Session Flow:
Concept of amplification
transistors
Construction of bjt
Operation
Current components
Configurations
Characteristics of bjt
Cut-off, active and saturation regions

## Slide 3
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
https://www.youtube.com/watch?v=HtXieQa0IlU

## Slide 4
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
https://www.youtube.com/watch?v=7ukDKVHnac4

## Slide 5
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 6
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
V
ID
VD
How to Increase VD?
By increasing V
By increasing ID
But V not to be increased.
Then How?
?
By Increasing Q
?

## Slide 7
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
V
ID
VD

## Slide 8
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Emitter
Heavily Doped
Moderate in Size
Base
Lightly Doped
Small in Size
Moderately Doped
Large in Size
Collector

## Slide 9
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Biasing:
Fixed Bias
Collector to Base Bias
Self Bias
Bias is direct current ( DC ) deliberately made to flow, or DC voltage deliberately applied, between two points for the purpose of controlling a circuit . In a bipolar transistor , the bias is usually specified as the direction in which DC from a battery or power supply flows between the emitter and the base.
setting a transistors DC operating voltage or current conditions to the correct level so that any AC input signal can be amplified correctly by the transistor. ➢ To active an transistor, biasing is essential.
Need for Biasing:
Types of Biasing:

## Slide 10
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
The circuit shown is called as a “fixed base bias circuit”, because the transistors base current, IB remains constant for given values of Vcc, and therefore the transistors operating point must also remain fixed. The collector current does not remain constant with variation in temperature or power supply voltage.
Fixed Bias:

## Slide 11
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 12
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Fixed Bias Circuit is often used in circuits where transistor is used as a switch. However, one application of fixed bias is to achieve crude automatic gain control in the transistor by feeding the base resistor from a DC signal derived from the AC output of a later stage. 1.
Uses of Fixed Bias:

## Slide 13
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
This circuit helps in improving the stability considerably. If the value of IC increases, the voltage across RL increases and hence the VCE also increases. This in turn reduces the base current IB. This action somewhat compensates the original increase.
Collector to Base Bias:
The collector to base feedback configuration ensures that the transistor is always biased in the active region regardless of the value of Beta (β). The DC base bias voltage is derived from the collector voltage VC, thus providing good stability.

## Slide 14
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Self-Bias. A better method of biasing is obtained by inserting the bias resistor directly between the base and collector, as shown in figure below. By tying the collector to the base in this manner, feedback voltage can be fed from the collector to the base to develop forward bias. This arrangement is called SELF-BIAS.
Self Bias:
This is also called the emitter follower for the same reason as the power supply follows the base bias and this stabilizes the Vbe. As the input changes or Vbb change, the power supply stabilization make the bias constant so that Vo remain constant and so self bias instead of external interference to stabilize out put.

## Slide 15
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
By Applying Thevenin’s Theorem to the input circuit, All the three circuits reduce to a single circuit as shown.
Fixed Bias
Collector to Base Bias
Self Bias

## Slide 16
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 17
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 18
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 19
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 20
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 21
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 22
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
h – Parameter Model:
Linear
Two Port Network
V1
V2
I1
I2
1
1’
2’
2
+
+
-
-
Dependent Variables:
V1, I2
Independent Variables:
I1, V2
V1 = h11 I1 + h12 V2
I2 = h21 I1 + h22 V2
V2 = 0.
i.e., output
Short Circuit
V2 = 0.
i.e., output
Short Circuit
I1 = 0.
i.e., input
Open Circuit
I1 = 0.
i.e., input
Open Circuit

## Slide 23
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
h – Parameter Model for transistor:
Transistor
Vi
Vo
Ii
Io
1
1’
2’
2
+
+
-
-
Dependent Variables:
Vi , Io
Independent Variables:
Ii , Vo
Vi = hi Ii + hr Vo
Io = hf Ii + ho Vo
Vo = 0.
i.e., output
Short Circuit
Vo = 0.
i.e., output
Short Circuit
Ii = 0.
i.e., input
Open Circuit
Ii = 0.
i.e., input
Open Circuit

## Slide 24
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
h – Parameter Model for Common Base:
Transistor
VEB
VCB
IE
IC
E
B
B
C
+
+
-
-
Dependent Variables:
VEB , IC
Independent Variables:
IE , VCB
VEB = hib IE + hrb VCB
IC = hfb IE + hob VCB
VCB = 0.
i.e., output
Short Circuit
VCB = 0.
i.e., output
Short Circuit
IE = 0.
i.e., input
Open Circuit
IE = 0.
i.e., input
Open Circuit

## Slide 25
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
h – Parameter Model for Common Emitter:
Transistor
VBE
VCE
IB
IC
B
E
E
C
+
+
-
-
Dependent Variables:
VBE , IC
Independent Variables:
IB , VCE
VBE = hie IB + hre VCE
IC = hfe IB + hoe VCE
VCE = 0.
i.e., output
Short Circuit
VCE = 0.
i.e., output
Short Circuit
IB = 0.
i.e., input
Open Circuit
IB = 0.
i.e., input
Open Circuit

## Slide 26
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
h – Parameter Model for Common Collector:
Transistor
VBC
VEC
IB
IE
B
C
C
E
+
+
-
-
Dependent Variables:
VBC , IE
Independent Variables:
IB , VEC
VBC = hic IB + hrc VEC
IE = hfc IB + hoc VEC
VEC = 0.
i.e., output
Short Circuit
VEC = 0.
i.e., output
Short Circuit
IB = 0.
i.e., input
Open Circuit
IB = 0.
i.e., input
Open Circuit

## Slide 27
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 28
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 29
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 30
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 31
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 32
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
The emitter follower is used
for impedance matching.
The emitter follower transistor is a design
which is basically a CC amplifier.
Emitter Follower:

## Slide 33
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 34
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
https://engineering.purdue.edu/wcchew/ece255s18/ece%20255%20s18%20latex%20pdf%20files/ece255Lecture_13_Feb27_BJT_Basic_Config.pdf

## Slide 35
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 36
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Example:
Solution:

## Slide 37
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Input Impedance:

## Slide 38
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Output Impedance:

## Slide 39
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 40
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 41
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN

## Slide 42
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Designing of CE Amplifier:
Design a CE amplifier with AV= -100,
IC=2mA, Ic(min)=1.75mA; IC(max)=2.25mA,
VCC =10V, RL =10KΩ, fL = 100Hz.
For BC107B hfe(min) =180; hfe(max) = 460

## Slide 43
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Design Equations:
At room temperature
VT=26mV

## Slide 44
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Using this data, we can calculate RC then RL.
Select VCE = 0.5VCC

## Slide 45
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
Now calculate RB using

## Slide 46
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
From the input loop equation
Design of Capacitors
If the lower cut-off frequency is fL and the upper cut-off frequency is fH, then the value of the emitter bypass capacitor C2 can be calculated from

## Slide 47
24EC2104 ELECTRONIC DEVICES & CIRCUIT DESIGN
The coupling capacitor C1 can be calculated from
The value of the coupling capacitor C2 can be calculated from