## Slide 1
Analog electronic Circuit Design
23ec2104
Topic:
Small-Signal Operation and Models
Department of ECE
Session - 07
AY-2025-2026
ODD SEM

## Slide 2: Session content
Trans-conductance
Input Resistance at the Base
Input Resistance at the Emitter
Voltage Gain
Separating the Signal and the DC Quantities
Hybrid-π Model
T Model

## Slide 3
AIM OF THE SESSION
To understand and analyze the small-signal behavior of Bipolar Junction Transistors (BJTs) using equivalent models for AC signal analysis.
INSTRUCTIONAL OBJECTIVES
The Session is designed to:
Define small-signal operation in BJTs and its purpose.
Explain the significance of small-signal models in amplifier analysis.
Describe the components of Hybrid-π and T-models.
LEARNING OUTCOMES
At the end of this session, learners will be able to:
Apply small-signal models for analyzing BJT amplifier circuits.
Derive and use small-signal parameters from DC operating points.
Choose the appropriate model (Hybrid-π or T-model) for different applications.

## Slide 4: Small-Signal Operation and Models

## Slide 5: Transconductance vBE = VBE + vbe-----(1)
If vbe ˂ VT,
-----(2)
-----(3)

## Slide 6: Transconductance
-----(3)
This approximation, which is valid only for vbe less than approximately 10 mV, is referred to as the small-signal approximation.
-----(4)
Thus the collector current is composed of the dc bias value
IC and a signal component ic ,

## Slide 7: Transconductance
This equation relates the signal current in the collector to the corresponding base–
emitter signal voltage. It can be rewritten as

## Slide 8: Transconductance

## Slide 9: Input Resistance at the Base
Thus,
where IB is equal Ic/β to and the signal component ib is given by
Substituting for IC/VT by gm gives
The small-signal input resistance
between base and emitter, looking into the base, is denoted by rπ and is defined as
Substitute gm and Replace Ic/β by IB

## Slide 10: Input Resistance at the Emitter
Thus,
where IE is equal to IC /α and the
signal current ie is given by
If we denote the small-signal
resistance between base and emitter looking into the emitter by re, it can be defined as

## Slide 11: Input Resistance at the Emitter
The relationship between rπ and re can be found by combining their respective definitions
Thus,
which yields

## Slide 12: Voltage Gain
Here the quantity VCE is the dc bias voltage at the collector, and the signal voltage is given by
Thus the voltage gain of this amplifier Av is

## Slide 13: Small Signal Operation
Input Resistance
at the Base
Input Resistance
at the Emitter
Transconductance
Voltage Gain

## Slide 14: Separating the Signal and the DC Quantities
Every current and voltage in the amplifier circuit of Fig.(a) is composed of two components: a dc component and a signal component
For instance, vBE = VBE + vbe, iC = IC + ic, and so on

## Slide 15: Separating the Signal and the DC Quantities
The dc components are determined from the dc circuit given in Fig. 6.36(b) and from the relationships imposed by the transistor.

## Slide 16: Separating the Signal and the DC Quantities
On the representation operation of
other hand, a of
the
the signal BJT can be
obtained by eliminating the dc sources, as shown in Fig.
Expressions for the current elements(ic, ib, and ie) obtained when a small signal vbe is applied.
Small-Signal Circuit Model.

## Slide 17: HYBRID π MODEL
This model represents the BJT as a voltage controlled current source
and explicitly includes the input resistance looking into the base , rπ

## Slide 18: HYBRID π MODEL
In this model

## Slide 19: HYBRID π MODEL
In this model
Ie=ic+ib

## Slide 20: HYBRID π MODEL
Slightly different model can be obtained by expressing the current of the controlled source (gmvbe) interms of base current ib
Equivalent circuit model is
Here the
transistor is
represented as a
controlled current
current- source,
with the control current being
ib.

## Slide 21: HYBRID π MODEL

## Slide 22: HYBRID π MODEL

## Slide 23: T Model
The current of the controlled source can be expressed in terms of the emitter current.
Ie=ic+ib
ib=ie-ic

## Slide 24: T Model
The current of the controlled source can be expressed in terms of the emitter current.

## Slide 25: T Model

## Slide 26: APPLICATION OF THE SMALL SIGNAL EQUIVALENT CIRCUIT
Eliminate the signal source and determine the dc operating point of the BJT and in particular the dc collector current IC.
Calculate the values of the small-signal model parameters:
3. Eliminate the dc sources by replacing each dc voltage source with a short circuit and each dc current source with an open circuit.

## Slide 27: APPLICATION OF THE SMALL SIGNAL EQUIVALENT CIRCUIT
Replace the BJT with one of its small-signal equivalent circuit models. Although any one of the models can be used, one might be more convenient than the others for the particular circuit being analyzed.
  Hybrid-π Model
  T Model
  Hybrid Model
Analyze the resulting circuit to determine the required
quantities (e.g., voltage gain, input and output resistance).