## Slide 1
Analog electronic Circuit Design
23ec2104
Topic:
BJT Characteristics
Department of ECE
Session - 02
AY-2025-2026
ODD SEM

## Slide 2: Session content
CE CONFIGURATION
INPUT CHARACTERISTICS
OUTPUT CHARACTERISTICS
REGIONS OF BJT OPERATION

## Slide 3
AIM OF THE SESSION
To demonstrate characteristics of BJT
INSTRUCTIONAL OBJECTIVES
This Session is designed to:
  Plot input characteristics of BJT
  Plot output characteristics of BJT
  Understand operating modes of BJT
LEARNING OUTCOMES
At the end of this session, you should be able to:
  Demonstrate input characteristics
  Demonstrate input characteristics
  Identify various modes of operation of BJT

## Slide 4: Common Emitter configuration
Fig. 2.1. depict the BJT configured for common emitter mode operation
Input voltage is applied across B-E junction with limiter resistance RB.
Output loop consists of variable voltage VCC, current limiter RC and output voltage of the BJT across collector and emitter, VCE For easiness to identify input loop and output loop the ground terminal is separated as shown in Fig. 2.2.
Fig. 2.1. CE configured BJT supplied with variable external voltages
Fig. 2.2. separation of ground terminal for ease of identification of input and output loops

## Slide 5
The Base Curve / Input Characteristics
Graph IB versus VBE
Like ordinary diode
Ohm’s law to Base loop
Ideal diode VBE = 0 and second app. VBE = 0.7 V
Fig. 2.3. Circuit operation to plot input characteristics
Fig. 2.4. Input characteristics of CE configured BJT

## Slide 6: Collector Curve / output Characteristics
Graph IC versus VCE
Ohm’s low to Collector loop
Fixed value of based current, vary VCC and measure IC and VCE
Fig. 2.5. Circuit operation to plot output characteristics
Fig. 2.6. Output characteristics of CE configured BJT for fixed base current
Fig. 2.7. Output characteristics of CE configured BJT for
Various values of input base current

## Slide 7
Analogy with Transistor in Active
Region: Fluid-jet operated Valve
In active region this stopper does not really have
noticeable effect on the flow rate
Emitter Base Junction – FB
Collector Base Junction – RB
Fig. 2.8. Analogy of fluid jet operation to active region of BJT

## Slide 8
Analogy with Transistor Cutoff
Fluid-jet operated Valve
Emitter Base Junction – RB
Collector Base Junction – RB
Fig. 2.9. Analogy of fluid jet operation to saturation region of BJT

## Slide 9
Analogy with Transistor Saturation
Fluid-jet operated Valve
The valve is wide open; changing valve position a little bit
does not have much influence on the flow rate.
E-B Junction – FB
C-B Junction – FB
Fig. 2.10. Analogy of fluid jet operation to cut-off region of BJT

## Slide 10
BJT

## Slide 11: BJT
Common Base Characteristics Input Characteristics
Output Characteristics

## Slide 12: BJT
Common Emitter Characteristics Input Characteristics
Output Characteristics

## Slide 13: BJT Circuits at DC Conditions and Models for the Operation of the BJT in Various Modes
Only DC Voltages are applied
Vbe=0.7 V and Vce=0.2 V

## Slide 14: BJT Circuits at DC Conditions and Models for the Operation of the BJT in Various Modes
Only DC Voltages are applied
Vbe=0.7 V and Vce=0.2 V

## Slide 15: BJT Circuits at DC Conditions and Models for the Operation of the BJT in Various Modes
Only DC Voltages are applied
Vbe=0.7 V and Vce=0.2 V

## Slide 16: BJT Circuits at DC-Active Mode(Problems)
Example, β is specified to be 100.

## Slide 17: BJT Circuits at DC-Saturation Mode(Problems)
Example, β is specified to be ATLEAST OF 50.

## Slide 18: BJT Circuits at DC-Cutoff Mode(Problems)
Example

## Slide 19: BJT operating regions
Fig. 2.11. Output and input characteristics of CE configured depicting possible operating regions
of BJT (active, saturation, cutoff)
With the analogy discussed, the operation of BJT is driven in to any of the three regions with base current value.
For this reason, BJT is termed as current controlled current source.
BJT acts as controlled switch when continuously operated in cut off and saturation regions
BJT acts as an amplifier when driven in to active region

## Slide 20: SuMMARY

## Slide 21
2.1 BJT shown in Fig. 2.12 has βDC of 300. Calculate IB, IC, VCE and PD.
Solution:
Example Problems
Fig. 2.12. CE Configured BJT biased with external voltages

## Slide 22
2.2 For the ideal BJT shown in Fig. 2.13 has βDC of 100. Determine VCE
Solution:
Example Problems
Fig. 2.13. CE Configured BJT biased with external voltages

## Slide 23
SELF-ASSESSMENT QUESTIONS
BJT is modelled as
Voltage controlled voltage source
Current controlled voltage source
Current controlled current source
Voltage controlled current source
What is the current in BJT in cut-off region
β IB
< β IB
Zero

## Slide 24
SELF-ASSESSMENT QUESTIONS
3. Which mode does BJT operate if B-E and B-C junctions are forward biased?
Saturation
Active
Cut-off
4. Which parameter shall be constant to plot input characteristics?
VCE
VBE
IC
IB

## Slide 25
C
C
A
A
ANSWERS

## Slide 26
TERMINAL QUESTIONS
Describe how to configure BJT in common emitter mode operation.
Discuss the input characteristics of BJT.
Discuss the output characteristics of BJT.
Draw output characteristics of BJT for various input base current values.
Derive the analogy between electron flow in BJT and jet flow in valve operated tube.
Identify the regions of operation of BJT

## Slide 27
REFERENCES FOR FURTHER LEARNING OF THE SESSION
Reference Books:
Albert Malvino, David Bate, “Electronic Principles”
Robert L. Boylestad and Louis Nashelsky - “Electronic Devices and Circuit Theory”

## Slide 28
THANK YOU
Team – Analog electronic Circuit Design
Prepared by – Mr. S. Ravi Teja